## Slide 1: ACT: Architectural Carbon Modeling Tools
@ MICRO 2022
Tutorial
Udit Gupta

## Slide 2: ACT Tutorial: Today
Time | Topic
1:00 – 1:15pm | Introductory remarks
1:15 – 1:30pm | Motivation: Understanding the source of computing’s emissions
1:30 – 2:15pm | Overview of ACT: An Architectural Carbon Modeling Tool
2:15 –2:30pm | Coffee Break
2:30 – 3:00pm | Hands-on ACT demo’s
3:00 – 3:15pm | Extending ACT
3:15 – 3:45pm | Office Hours
3:45 – 4:00pm | Closing remarks
Notes: Finally, given our understanding of carbon emissions, we will conclude by charting paths for how to design future sustainable computing systems.

## Slide 3: Sing up on our Google form!
https://forms.gle/hEAju2suaeEnisRQA

## Slide 4
Estimating the embodied footprint of 2 devices using ACT
Takeaways
ACT provides first-order approximate of LCA’s that use old technology nodes (45nm NAND, 32nm CPU)
ACT enables architects to study new technology nodes
IC component | ACT vs. Dell R740 server LCA | ACT vs. Fairphone 3 mobile device LCA
Compute (processors, SoC’s) | Within 2.2x | Within 1.18x
Memory | Within 1.62x | Within 2.1x
Storage | Within 1.05-2.2x | 

## Slide 5
How to set up ACT
>$ git clone https://github.com/alugupta/ACT.git
>$ cd ACT/
>$ source setup.sh
>$ python model.py
[Fab logic] Carbon/area from energy consumed 1209.5
[Fab logic] Carbon/area from gasses 240
[Fab logic] Carbon/area from materials 500
[Fab logic] Carbon/area aggregate 2228.0
https://github.com/alugupta/ACT

## Slide 6
Estimating embodied footprint of Fairphone 3
Full end to end example can be found here: https://github.com/alugupta/ACT/blob/main/exps/fairphone3/fairphone3.py
https://www.fairphone.com/wp-content/uploads/2020/07/Fairphone_3_LCA.pdf
# Make sure you are in root directory
>$ cd ACT
>$ python tutorial/fairphone3_tutorial.py
--------------------------------
ACT RAM + Flash 0.0 kg CO2 vs. LCA 11 kg CO2
ACT CPU 0.0 kg CO2 vs. LCA 1.07 kg CO2
ACT ICs 0.0 kg CO2 vs. LCA 5.3 kg CO2

## Slide 7
Estimating embodied footprint of Dell R740
Full end to end example can be found here: https://github.com/alugupta/ACT/blob/main/exps/dellr740/dellr740.py
https://corporate.delltechnologies.com/content/dam/digitalassets/active/en/unauth/data-sheets/products/servers/lca_poweredge_r740.pdf
# Make sure you are in root directory
>$ cd ACT
>$ python tutorial/dellr740_tutorial.py
--------------------------------
ACT SSD main 0 kg CO2 vs. LCA 3373 kg CO2
ACT SSD secondary 0 kg CO2 vs. LCA 64.1 kg CO2
ACT DRAM 0 kg CO2 vs. LCA 533 kg CO2
ACT CPU 0 kg CO2 vs. LCA 47 kg CO2